## Slide 1: Relay based H Bridge
TEARCI T3 Julio filho
Tomás carvalho
Luís amorim

## Slide 2: Summary
Intro
Physical assembly
Schematic assembly
Technical details
Final thoughts

## Slide 3: INTRO
The H bridge

## Slide 4
The beginning
Initially, we received an assignment to assemble an H-bridge for a motor, where we would be assembling our own relay shields.

## Slide 5: Physical assembly
My first steps in the project

## Slide 6: The relay Shield & H Bridge
My setup simulating the relay shield and its operation.
A simulation with 4 relays using pre-made optocouplers.

## Slide 7: Schematic
Complete schematic with 2 shields with dual relays joined in a single H-bridge design.

## Slide 8: PCB
Images of the project's PCB made in KiCad (left) and then images of the Gerber viewers (right).

## Slide 9: Some thechnical details
A deeper dive into some information I had to look up during the project's production.
The Arduino pin cannot supply the relay coil current (~70 mA) → use an NPN transistor as a low-impedance switch
Design for saturation using forced β ≈ 10
→ IB ≥ IC / 10
Coil current: IC ≈ Vcoil / Rcoil ≈ 5 V / 70 Ω ≈ 72 mA
Therefore, IB ≈ 7.2 mA
Base resistor: RB ≈ (VOH(min) − VBE(sat)) / IB
Using VOH(min) ≈ 4.1 V, VBE(sat) ≈ 0.8 V → RB ≈ 458 Ω → choose 220+220 Ω
The overvoltage protection diode in the coil protects against voltage spikes during shutdown